581333   Data Communication I

Separate Examination  11.11.2003

Write the name of the course, date, your name,  student number or birth date  and signature on every separate sheet. Books and calculators are not allowed.

1.TCP/IP protocol stack  and  TCP/IP network  (20 p)

a)  Show the TCP/IP protocol stack  and name its layers.  Put protocols   PPP, DNS, UDP and

ARP to  correct layers  in  the  TCP/IP protocol stack. (8 p)

b)  Draw a picture of  a TCP/IP network  consisting of hosts and routers,  of  trunk lines and of

LANs connected by   bridges, switches and hubs.(4 p)

c)  What kind of device is a repeater? (2 p)

d)  What layers of the  TCP/IP  protocol stack have to be implemented in the devices of b) and c)

i.e. in   routers, hosts, hubs, switches, bridges and  repeaters? (6p)

2. Packets sent by the sender to a network can arrive corrupted to  the receiver or even get totally lost in the network.

a) What factors are causing packet losses  and errors in packets?( 4 p)

b) How does the receiver detect corrupted packets and packet losses? What  different means and

methods can be used? How does the system recover from this kind of error situations? (8 p)

c) How do the Internet protocols IP, UDP and TCP react to errors? How do these protocols

handle errors,  recover from errors or try to prevent error  from happening? ( 8 p)

3. About addresses in the Internet

a) The  link  http://www.motorola.com/NSS/Technology/cdma.html   is clicked by a web  surfer.

What do the different parts of this address mean? (3 p)

b) What kind of addresses are used in the  different layers of the  Internet protocol  stack ? ( 8 p)

c) Explain  how,  in the different protocol layers, does the upper layer get to know the address

that is used  in the layer below. ( 9 p)

581333  Tietoliikenne I

Erilliskuulustelu  11.11.2003

Kirjoita jokaisen vastauspaperisi yläreunaan kurssin nimi ja kokeen päivämäärä sekä nimesi, syntymäaikasi ja allekirjoituksesi.

1.  TCP/IP-protokollapino ja TCP/IP-verkko (20 p)

a) Piirrä TCP/IP-protokollapino ja nimeä sen eri kerrokset sekä aseta TCP/IP-protokollapinon

oikeisiin kerroksiin  protokollat PPP, DNS, UDP ja ARP? (8 p)

b) Piirrä kuva TCP/IP-verkosta, jossa on sekä isäntäkoneita että reitittimiä, runkoverkko,

silloilla (bridge), kytkimillä (switch) ja  keskittimillä (hub) yhteenliitettyjä lähiverkkoja. (4 p)

c)  Millainen laite on toistin (repeater)? (2 p)

d) Mitkä TCP/IP-protokollapinon kerrokset on toteutettava b) ja c) kohtien laitteissa  eli

reitittimissä,  isäntäkoneissa, keskittimissä, kytkimissä, silloissa ja  toistimissa? (6p)

- Lähettäjän verkkoon lähettämät paketit voivat  saapua vastaanottajalle virheellisinä tai jop   kadota kokonaan.

a)  Mitkä tekijät aiheuttavat virheellisiä paketteja tai pakettien katoamisia?   (4 p)

b)  Miten vastaanottaja havaitsee paketin virheelliseksi tai huomaa paketin  puuttuvan? Mitä

keinoja ja tapoja tähän on käytettävissä? Miten tällaisesta virhetilanteesta toivutaan? (8 p)

c)  Miten Internet-protokollat IP, UDP ja TCP suhtautuvat virheisiin ja  virhetilanteesta

toipumiseen? (8 p)

3. Internetin osoitteista (20 p)

a) Linkkiä http://www.motorola.com/NSS/Technology/cdma.html  klikataan WWW-verkossa .

Mitä tämän osoitteen eri osat tarkoittavat? (3 p)

b) Millaisia osoitteita on käytössä  Internetin protokollapinon eri kerroksilla? (8 p)

c) Miten  eri protokollakerroksilla ylempi kerros selvittää alemman  kerroksen  käyttämän

osoitteen? (9 p)